## Slide 1: IR simulations update: luminosity monitor (mostly)
Richard Petti (BNL)
EIC Task Force Meeting
05-07-2015

## Slide 2: Outline
generalities of a luminosity monitor
reminder of luminometer design at eRHIC
quantification of the required acceptance
notable code developments
  DJANGOH
  eicsmear
  EicRoot

## Slide 3: Measuring Luminosity
closely follow the implementation by ZEUS (HERA II)
measure the process e+p -> e+p+gamma
  high rate
  pure QED with precisely calculable cross section
  luminosity related to measured rate of photons

## Slide 4: A design for eRHIC
IP
Legend:
Hadron magnets – blue
electron magnets– red
brem photon transport line – yellow
electron bending dipole
low Q2 tagger (~15m)
pair spec dipole (~33m)
lumi calorimeters (~45m)
+y
-z
+x

## Slide 5: Requirements for the acceptance of photons
need to give CAD a number for the angular acceptance needed for photons
requirement coming from:
  the angular distribution of photons coming directly from the physics process
  the angular spread of said distribution from beam effects (emittance, crossing angle, etc.)

## Slide 6: Distribution of photons from physics
Bethe-Heitler calculation (1934)
energy distribution
angular distribution

## Slide 7: How do the distributions look for eRHIC collisions?
code obtained from B. Schmidke to generate these distributions
integrated cross section of 136 mb
0.015 mrad

## Slide 8: Effect of radiative corrections
[1] Precision calculation of processes used for luminosity measurement at the ZEUS experiment, T.Haas, V.Makarenko, arXiv:1009.2451v2
include various one-loop QED radiative corrections
note: the following is a comparison of calculations done at 27.6 x 920 GeV ep collisions
corrections are small

## Slide 9: DJANGOH simulations
use DJANGOH to study effect of rates in polarized ep collisions
  calculation/code not yet in existence, but this is the end goal
some trouble getting the simulations running
  problems with tuning/processes called
  software issues (discussed later)

## Slide 10: DJANGOH event simulation
tuning parameters (some are modified from my input, I put the actual range used)
  1.3056e-11 < x < 0.99
  1e-10 < Q^2 < 1 GeV2^2
  Wmin = 0.938 GeV
  1.3e-11 < y < 0.95
caveats:
  get the message: Warning: lower limit in x and/or Q2 too small for DIS formalism
  lots of: Error in LYSTFU: x = +Infinity outside physical range
  program enters SOPHIA module (for hadronization?) but fails (nothing to hadronize)
  events seem to be mediated by Z_0 (pdg = 23) bosons, not photons!

## Slide 11: Comparison of DJANGOH simulation with Bethe-Heitler
** ELASTIC TAIL:
ELASTIC EP WITH CORRECTIONS 9.0308E+08 +/- 9.0308E+04 NB
INITIAL STATE LEPTONIC RADIATION 1.6597E+08 +/- 3.3521E+06 NB
FINAL STATE LEPTONIC RADIATION 1.6125E+08 +/- 1.1234E+06 NB
COMPTON CONTRIBUTION 3.9081E-01 +/- 3.5560E-01 NB
** TOTAL CROSS SECTION: 1.2303E+09 +/- 3.5365E+06 NB
absolute scaling
relative scaling (please ignore numbers on yaxis)
observe some difference – still in the tuning?

## Slide 12: Angular emittance of the beam
taken from the eRHIC design study Table 3-1 (pg. 48)
  emittance = 23e-6m (58e-6m) for ep (eAu)
  beta* = 5cm

## Slide 13: Summary of needed luminometer acceptance
from the machine:
  0.1 – 0.35 mrad from beam divergence
from physical process:
  0.05 mrad (negligible)
total
  0.4 mrad
  still effects from crossing angle? small, see later slides

## Slide 14: Code Developments

## Slide 15: DJANGO debugging (I)
the package as existing in the PACKAGES directory was not functioning
first a complaint about a mismatch in version of lha library expected vs what is loaded
  line 13476 of djangoh_h.f needed to change lhaverdef=‘5.8.6’ to lhaverdef=‘5.9.1’
segmentation fault due to line 2179 of lhaglue-5.9.1-copy.f
  loop over nsets, but nsets is total number of pdf sets, which is large
  causes loop to exceed the array length of mxset = 3
  we initialize nset=0 and also change the loop to end at nmxset rather than nsets
  this fixes the seg fault
complaint of not finding polarized pdf (when running in unpolarized mode)
  needed to modify function HSFG in django_u.f
  change code so that function call to HSDPVR is only made if HPOLAR.ne.0, i.e. this function is only called if we are doing polarized beam collisions
one more fix, found when compiling with –bounds-check
  line 261 of djangoh_u.f
  loop range was 0,10
  Fortran arrays start at 1, not 0

## Slide 16: DJANGO debugging (II)
event record issue, no scattered proton in the record
  seems that the scattered proton (for elastic events) is not written out in the event record
  found a fix, modified sophia.f file near line 183
  sophia gets called, but hadronization fails for this type of process (as it should for these elastic events)
  added a statement that if there is nothing to hadronize, then just grab scattered proton information from the HEPEVT common block
when going to much lower Q^2, received an error that stopped the program
  received complaint that Q2min is outside the DIS regime
  the LST(3) flag sets what to do in case of this type of warning
  default is set to 2, which causes program to complain and stop execution
  added a code word usable from the input file to change this (WARNING is the code word)
  new value set LST(3) = 1, which causes the program to complain, but to continue running anyway

## Slide 17: Code developments: eicsmear (I)
further development of eicsmear (not in svn yet)
new arguments can be passed to BuildTree() function
  this function takes an input ASCII file from MC generators and produces a root file with a standard EICTree format
    1) argument to allow user to give each event a non-zero event vertex
    2) argument to allow user to give a crossing angle
    3) argument to allow user to give angular beam emittance
a bit on the implementation:
  added a new singleton class, EventVertexParameters
    this class stores information related to the event vertex
  an instance of this class can be called from anywhere in the program and always returns the same instance

## Slide 18: Code developments: eicsmear (II)
event vertex smearing
  input desired smearing parameters to arguments of BuildTree()
  smears the x, y, and z position from user specified width
  smear according to gaussian or uniform depending on users preference
  this shifts the vertex position of ALL tracks in the event
  stored in the event tree as xVertex, yVertex, zVertex
crossing angle
  ported Alexander’s code into the eicsmear package
  it calculates the boosts and rotations needed to transform the lab frame kinematics with a crossing angle to the lab frame scenario without a crossing angle
  then the reverse operation of these boosts and rotations occur on the product particles of the collision
angular beam divergence
  the angular beam divergence is randomly generated on a per event basis based on the emittance provided by the user in the BuildTree() function
  this generated angle is added to the crossing angle (which is negligible in comparison) before the boost and rotation matrices are calculated

## Slide 19: Effect of crossing angle?
crossing angle leads to a negligible effect on angular distribution of photons
note: the electron beam is taken along z-axis

## Slide 20: crossing angle effect on protons?
no mod
10mrad crossing angle
10mrad crossing angle + 0.1mrad emittance
100mrad crossing angle

## Slide 21: Proof of event vertex smearing

## Slide 22: Code development: EicRoot
Note: changes not yet pushed to SVN
modified the functionality of the BeamPipeGeoParData class to allow for intersecting sections of beam pipe
maybe the installation process can be streamlined for the user, but it works for now

## Slide 23: General view of the current IR design implementation
electrons
Legend:
beam pipe
hadron magnet apertures
electron magnet apertures
+y
-z
+x

## Slide 24: General view of the current IR design implementation
electrons
Legend:
beam pipe
hadron magnet apertures
electron magnet apertures
IP
roman pots
low Q2 tagger
photon transport line with Al exit window
dipole magnet for pair spectrometer
emcals for lumi monitor

## Slide 25: General view of the current IR design implementation
electrons
Legend:
beam pipe
hadron magnet apertures
electron magnet apertures
0 m
-4.55 m
4.55 m
-15 m
-31 m
-33m
-45 m
18 m
+y
-z
+x

## Slide 26: Backward Direction (electron going side after the IP)
+y
-z
+x
electrons
low Q2 tagger

## Slide 27: Backward Direction (electron going side after the IP)
electrons
-31 m
-33m
-45 m
-z
+x

## Slide 28: A little bit on the low Q2 tagger…
finally returning to the low Q2 tagger simulation after working on the lumi design
basic design implemented
next step is to make the simulation more realistic
  add a third tracking layer and do real track reconstruction
  estimate the expected energy resolution given a realistic emcal design

## Slide 29: next iteration of the low Q2 tagger design
previous implementation of emcal was not very realistic
was looking at pure MC hits in the previous iteration
  Alexander did some code work on EicRoot to allow me to digitize hits for my combined tracker/emcal detector so that I can take the next step in sims
implementation probably not long enough for full shower development
  can play with materials and simulation parameters to adjust this, but this is probably true
only considered active material before
  now implemented a design with a crystal encased in inactive material more similar to a realistic design
  play with the thickness of the absorber material
increasing the tower length and looking to see the effect
finding that lots of tracks actually deposit energy at the edge of the detector, causing loss of energy
  screen shots on next slide
will study the energy reconstructed as a function of distance from detector edge and electron energy
will study the existing clustering algorithm in more detail
  just running as a black box at the moment

## Slide 30: some event displays

## Slide 31: how well is the energy of the electron reconstructed?
reconstructed energy
true track energy

## Slide 32: test hypothesis of poor energy resolution because hits at edge
simply widen and move detector over and see if things change
  of course this cannot be realistically done since there is a beam there!!
probably obvious, but it significantly helps the energy reconstruction
reconstructed energy
true track energy

## Slide 33: Transverse size of shower in emcal
quantified by the Moliere radius
need to contain shower to a few cm radius
http://www.kip.uni-heidelberg.de/~coulon/Lectures/Detectors/Free_PDFs/Lecture9.pdf
CMS emcal:
  lead tungstate (PbWO4) cyrstals
  RM = 2.2cm
  ρ = 8.3g/cm3
  22x22 mm2 at front
  26x26 mm2 at back
  230 mm length
  X0 = 25.8
  crystals contained within thin-walled glass-fiber alveola
http://cds.cern.ch/record/922757/files/lhcc-2006-001.pdf

## Slide 34: Simulations with PbWO4 ecal
just implemented the PbWO4 material this morning
ran some quick simulations…definitely improved compared to previous (diamond sensor material) study, but still not great
currently generating more events to look more differentially (function of scattering angle as well as energy)
(old) diamond sensor
PbWO4 crystal

## Slide 35: Summary
Code developed for general simulation tools
  DJANGOH
  eicsmear
  EicRoot
Closing in on acceptance requirements for a luminosity monitor at eRHIC
resuming detailed simulations of the low Q2 tagger
To do:
  run some real event simulations to get acceptance for luminosity monitor
  make beam pipe setup more automatic
    define sections from magnet geometry files
  return to low Q2 tagger simulations and get a more accurate measure of the resolution of the detector
    carefully consider possible materials for the emcal (PbWO4?)
  roman pots – investigate effect of additional stations
  think about a paper once things are at a sufficient level and some dust settles

## Slide 36: Backups

## Slide 37: Crossing angle details
start with collision of ep, with e along z axis and p at an angle to the z axis
boost the particles to the center of mass system, which has inherent angle from z axis
rotate system so that particles align on z axis
boost back to lab frame
the matrices used to do this are stored in the EventVertexParameters class
this process is reversed for the products of the collision